## Slide 1: Computer-Aided Design (CAD) Competition

## Slide 2
Overview
Objectives
Background
Materials
Procedure
Report/Presentation
Closing

## Slide 3
Objectives
Understand the simulation capabilities of Fusion 360, a common computer-aided design (CAD) software
Use the basics of modeling techniques in Revit
Develop product evaluation and minimal design skills

## Slide 4
What is Fusion 360?
Fusion 360 is a cloud-based computer-aided design software
Allows engineers to make precisely scaled drawings that are turned into 3D models to visualize concepts or functionality
Runs tests to imitate real-world situations
Almost identical to SolidWorks and a major upgrade from Inventor in terms of accessibility and ease of use

## Slide 5
What is Autodesk Revit?
Revit is a building modeling software for architects and engineers
Allows users to design buildings and other architectural structures in 3D while allowing for 2D drafting elements
Can be used to track stages of a building’s lifecycle, from creation to demolition

## Slide 6
Background Information
Simulation in Fusion 360 – Static Stress
  Simulates the linear responses to a force being applied to an object based on the material, constraints, and points of application
  Analyzes the deformation, stress, and safety factor in a model from structural loads and constraints
  Can determine whether an object is ready to sustain real-world loads or needs to be remodified
  The resultant safety factor is the measure of how much load a object can sustain before permanent deformation or fracture

## Slide 7
Background Information
3D Modeling in Revit
  Used for creating homes, buildings, and structural support systems
  Used to create floor, plumbing, electric, and heating, ventilation, and air conditioning (HVAC) plans
  Capable of viewing models in three dimensions and walking through the structure floor by floor

## Slide 8
Materials
Computer
Fusion 360
Autodesk Revit
Predesigned parts

## Slide 9
Procedure – Fusion 360
Determine the location, magnitude, and direction of the force, as well as material and location of constraints
Run a stress test on the predesigned part given to you
Review factor of safety and location of fracture, then use Fusion 360 to add the modifications onto the model without changing the main base
Rerun tests and remodify until part has safety factor of at least 3

## Slide 10
CAD Competition
Redesigned part must be less than double the initial volume
Safety factor must be at least 3
Cannot alter the applied forces, fixed point constraints, and areas highlighted in red on model

## Slide 11
Revit Problem Statement
Create a 350 – 400 square foot apartment for residents/college students
Contains one of each: bathroom, bed, kitchen, table, desk
Must have sufficient lighting (at least 1 window)
A floor plan layout of the entire apartment
An electrical plan for the entire apartment

## Slide 12
Procedure – Revit
Sketch out the apartment based on the problem statement
Create the floor plan on Revit
Insert all required furniture and appliances
Create electrical plan on the same Revit file

## Slide 13
Report/Presentation
Submit a Revit file before the end of lab
Individual lab report
Milestone 1 Presentation is next week
CAD Competition presentation is the following week

## Slide 14
Closing
Have all lab notes signed by TA
Each team member should have turn using software
Save all files
Submit all work electronically
Return all unused materials to TA
Extra credit will be awarded by your professor for the best Revit design!

## Slide 15
CAD Competition
QUESTIONS?