## Slide 1: INTRODUCTION TO DIGITAL LOGIC
EG1004 | LAB 5

## Slide 2: OVERVIEW
Objective
Background Information
Materials
Procedure
Assignment
Closing
1
Figure 1: Semiconductor Courtesy of Scoop.it

## Slide 3: OBJECTIVE
To design a combinational logic circuit for a given problem statement
To build and test the circuit on a breadboard
2

## Slide 4: BACKGROUND INFORMATION
Digital logic:
  Conceptual language behind modern computer systems
  Two values of true and false (1 and 0) that lead to complicated decisions
Truth table – shows all the possible input combinations and their associated outputs (example on next slide)
3
Figure 2: Boolean Circuit Courtesy of All About Circuits

## Slide 5: BACKGROUND INFORMATION
Think of this example
An ATM has three options:
  Print statement
  Withdraw money
  Deposit money
The ATM will charge a fee when:
  Money is withdrawn
  A statement is printed without depositing money
Table 1: Truth Table for ATM Example
4
Inputs |  |  | Output
P (Print) | W (Withdraw) | D (Deposit) | C (Charge)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 6: BACKGROUND INFORMATION
Logic gates:
  NOT gate – inverts the input
  AND gate – both inputs must be true for the output to be true
  OR gate – if either input is true the output will be true
Table 2: Logic Gates
5
 | NOT | AND | OR
Symbol |  |  | 
Arithmetic Operation |  |  | 
# of Inputs | 1 | 2+ | 2+
 | NOT | AND | OR
Symbol |  |  | 
Arithmetic Operation |  |  | 
# of Inputs | 1 | 2+ | 2+

## Slide 7: BACKGROUND INFORMATION
Boolean equation – mathematical representation of all the combinations in the truth table that yield an output of 1
Represents when a fee is charged in the ATM example
Table 3: Truth Table for ATM Example with True Combinations
6
Inputs |  |  | Output
P (Print) | W (Withdraw) | D (Deposit) | C (Charge)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 8: BACKGROUND INFORMATION
Karnaugh map (K-map) – two-dimensional representation that shows the common characteristics of the inputs
Only one value can change at a time between adjacent rows and columns
Table 4: K-map for ATM Example
7
 | 0 | 1 | 1 | 1
 | 0 | 1 | 1 | 0
 | 0 | 1 | 1 | 1
 | 0 | 1 | 1 | 0

## Slide 9: BACKGROUND INFORMATION
Simplified Boolean equation – mathematical representation of true values in the K-map
  Box together 1s in the K-map
  Number of cells in a box must be a power of 2 (1, 2, 4, 8, etc.)
  Look for the biggest boxes first
  Boxes can overlap
Simplified equation is determined by constant variable(s) in each box
Table 5: Simplified Boolean Equation for ATM example
8
 | 0 | 1 | 1 | 1
 | 0 | 1 | 1 | 0
 | 0 | 1 | 1 | 1
 | 0 | 1 | 1 | 0

## Slide 10: BACKGROUND INFORMATION
Combinational logic circuit – graphical representation of the simplified Boolean equation
9
NOT
AND
OR
Figure 3: Combinational Logic Circuit for ATM Example

## Slide 11: BACKGROUND INFORMATION
10
Minimization of Boolean functions
  K-map used to simplify complex Boolean equations
  Reduces complexity of logic circuit
  Would increase efficiency and decrease cost in implementation
Figure 4: Complex Logic Circuit (Left) vs.
Simplified Logic Circuit (Right)

## Slide 12: BACKGROUND INFORMATION
Integrated Circuits (ICs) – chips that consist of small assemblies of electronic components
Logic Gate ICs consist of logic gates that can be used to prototype combinational logic circuits on a breadboard
11
Figure 5: Diagram of NOT/AND/OR IC Chips

## Slide 13: BACKGROUND INFORMATION
12
Figure 6: Diagram of the example ATM circuit
Print (P)
Withdraw (W)
Deposit (D)

## Slide 14: MATERIALS
A 7432 IC (4 dual-input OR gates)
A 7408 IC (4 dual-input AND gates)
A 7404 IC (6 single-input NOT gates)
Breadboard
5V Battery Case
LED
220 Ω Resistor
Slide Switches
Wires
13
Figure 7: Integrated circuit (IC) chips courtesy of Wikipedia

## Slide 15: PROBLEM STATEMENT
Farmer Georgi has a hen on his 350-acre farm that produces high-quality eggs
To protect the hen from a fox who has been wandering around the farm and his corn, he needs an alarm system
14
Figure 8: Farmer Georgi’s Farm Courtesy of ThoughtCo

## Slide 16: PROBLEM STATEMENT
Farmer Georgi has two barns
  Think of Barn A as “0” and Barn B as “1” in the truth table
A fox, hen, and corn can be in either barn at anytime
Design an alarm system that will sound when:
  The fox and hen are in the same barn
  The hen and corn are in the same barn
15

## Slide 17: PROCEDURE
Part I: Formulate the Simplified Boolean Equation
Build a truth table for the alarm system
Create a Boolean equation
Build a K-map
Create a simplified Boolean equation
Draw a combinational logic circuit
  Add a light bulb to represent the alarm
16
Figure 9: IC Chip

## Slide 18: PROCEDURE
Part II: Test the IC Chips
Use the Arduino board setup by the TAs to test the NOT/OR/AND IC chips
The Arduino program will determine if the IC chips are functional or not
Orient the IC chips properly
17
Figure 10: IC chip tester

## Slide 19: PROCEDURE
18
Figure 11: Diagram of NOT/AND/OR IC Chips
Part III: Build the Combinational Logic Circuit
Build and test the logic circuit on a breadboard
  Wire the combinational logic circuit using the IC chips
  Power (+5V) and ground the IC chips
  Orient the IC chips properly

## Slide 20: ASSIGNMENT
Individual lab report:
  Answer discussion questions in manual
  Explain how k-maps help simplify the circuitry
  Include the truth table, both Boolean equations, and k-map
  Include pictures of the completed logic circuit
  Due at 11:59 PM the night before Lab 6
Team presentation:
  Address discussion points in manual
  Include pictures of the completed logic circuit
19

## Slide 21: CLOSING
Take pictures of the completed logic circuit
Clean up workstations
Return all unused materials to the TA
20

## Slide 22: QUESTIONS?