## Slide 1: Boom Construction
Notes: L.Mexhitaj 2009

## Slide 2: Overview
Objectives
Background
Materials
Procedure
Rules of the Competition
Report / Presentation
Closing

## Slide 3: Objectives
What is a boom?
How and why do materials fail?
  Stress and strain
Design light-weight boom to hold significant load
Understand factors engineers consider when designing a boom
Construct and test boom

## Slide 4: Boom
Lifts and moves heavy objects
  Objects usually much heavier than the boom
Examples
  Construction cranes
  Computer monitor arms
  Cantilever bridges
  Rotating bridges

## Slide 5: Common Structural Modes of Failure
Corrosion
Thermal cycling
Thermal Shock
Breakage under load
  Instant fracture
  Delayed response (fatigue)

## Slide 6: Corrosion
Exposure to caustic chemicals for extended periods
Substances and material react
  Material weakened by being “eaten away”
Examples
  Iron rusting (exposing iron to water)
  Wind blowing sand on rocks, bridges, etc.
  Acids
  Water (rust)
  Salt
  Air (oxidation)

## Slide 7: Thermal Cycling
Material’s temperature changes continuously over time
Material cracks or shatters due to stresses created by expansion/contraction
Example
  Elastic in clothes cracks once removed from clothes dryer

## Slide 8: Thermal Shock
Material undergoes extreme temperature changes in a short time period
Mixed temperatures throughout material cause compression/expansion resulting in cracks
Example:
  Hot glass bottle placed into ice cold water, bottle would explode and shatter

## Slide 9: Breakage Under Load
Maximum load supported by material is exceeded
Material cracks/crumbles (ie. Thermal shock)
Over usage
  Too many load cycles

## Slide 10: Breakage Under Load
Maximum load supported by material is exceeded
Material cracks/crumbles (ie. Thermal shock)
Over usage
  Too many load cycles

## Slide 11
Stress and Strain
Stress: measure of internal force that keeps material together
  Resists form change of body
Strain: measure of deformation (elongation/compression) of material
  Change from original dimension
Examples
  Stretching of rope while pulling
  Car tire under load

## Slide 12: Stress - Strain Figure
DL=Change in length
Lo=Original length
F= Applied force
A = Cross-sectional area
Lo
D L
Load F
Cross-sectional area of bar
Fixed Support
Stress (s) = F
A
Strain (e) = DL
Lo

## Slide 13: Stress - Strain Graph
Key points/regions
  U.T.S.
  (Ultimate Tensile Strength)
  Fracture Stress
  Elasticity Region {E}
  Plasticity Region {P}
Strain (e)
[in/in]
Stress (s)
[psi]
Fracture
Stress
U.T.S.
{P}
{E}

## Slide 14: Ultimate Tensile Stress (sm)
Greatest amount of stress material will withstand without failing
Plastic instability occurs when past U.T.S.
U.T.S. = Pmax
Ao
Pmax = Applied force
Ao= Cross-sectional
area
Stress (s)
[psi]
Fracture
Stress
U.T.S.
{P}
{E}
Strain (e)
[in/in]

## Slide 15: Fracture Stress (sf)
Stress at which the material completely fails
Fracture Stress = Pf
Ao
Pf = Applied Force
Ao= Cross Sectional
Area
Stress (s)
[psi]
Fracture
Stress
U.T.S.
{P}
{E}
Strain (e)
[in/in]

## Slide 16: Elasticity Region
Strain will disappear when stress is removed
Stress and strain vary linearly, obeying Hooke’s Law  s  e
Stiffness of material found by Young’s Modulus of Elasticity:
E= s/e
(slope of elastic region)
Stress (s)
[psi]
Fracture
Stress
U.T.S.
{P}
{E}
Strain (e)
[in/in]

## Slide 17: Plasticity Region
Strain will NOT disappear when stress is removed
  Permanent deformation
Range of plasticity:
  Ductile materials deform considerably before fracture
  Brittle materials do not deform much and failure occurs suddenly
Stress (s)
[psi]
Fracture
Stress
U.T.S.
{P}
{E}
Strain (e)
[in/in]

## Slide 18: Stress - Strain Example
The Plastic Pen Cap and Nervous Student
1. Elastic Region - Student applies force, bending tip of pen cap back. When force is removed, tip of cap returns to original position.
2. Plastic Region - Student twists and bends tip of cap. When force is removed, the tip of cap stays mangled.
3. U.T.S. - Student bends cap some more. Cap still in one piece, but certain areas are very weak and on the verge of breaking.
4. Fracture Stress - Student bends cap one more time. The cap finally breaks into 2 pieces.
1
2
3
4

## Slide 19: Materials for Lab
2 thin dowels (5/16” dia. x 48”)
2 thick dowels (7/16” dia. x 48”)
6 12” bamboo skewers
Cellophane Tape
Kevlar string

## Slide 20: Setup for Testing

## Slide 21: Competition Ratios
Unadjusted Ratio
Adjusted Ratio
NOTE: Adjusted ratio used to determine winner

## Slide 22: Rules of Competition
Design specifications
  TA initials and dates sketches of design before materials are distributed
  Materials may be cut and arranged in any way
  Boom must extend a horizontal distance of at least 1.5m after mounting
  Construction must be completed in time allotted
  No more than 2 minutes to anchor boom
  Weight will be added until boom deflects 0.2m
Design Specifications
Disqualifications
Declaration of winners

## Slide 23: Rules of Competition
Disqualifications
  Design is less than 1.5m horizontally when mounted
  Exceed 2 minute max time for anchoring boom
  Boom must only touch anchor
  (4” dia. pipe)
Design Specifications
Disqualifications
Declaration of winners

## Slide 24: Rules of Competition
Declaration of winners
  Design with highest adjusted ratio wins competition
  Decision of TA is FINAL
Design Specifications
Disqualifications
Declaration of winners

## Slide 25: Procedure
Boom design
  Observe provided materials
  Brainstorm design strategy with team members
  Note design decisions and necessary design changes
  Sketch proposed design
  Have TA initial sketch and notes
  Build boom according to sketch
Boom Design
Test
Post-Test

## Slide 26: Procedure
Test
  TA will create a spreadsheet to record competition results
  Weigh boom and announce value to TA
  When instructed, fasten boom to anchor
    Announce when “DONE!”, to record time
  TA measures length from tip of anchor to weight mounting point on boom
    Must meet 1.5m requirement
  Add weights until boom deflects 0.2m vertically, or fails
Boom Design
Test
Post-Test

## Slide 27: Procedure
Post-Test
  TA announces winner of competition
  (team with largest adjusted ratio)
  Copies of spreadsheet available to all teams on eg.poly.edu
  TA initials and scans original data
Boom Design
Test
Post-Test

## Slide 28: Assignment: Report
Team Lab Report
Title Page
Discussion topics in the manual
Include original data with TA’s signature
Include class results and photo of boom

## Slide 29: Assignment: Presentation
Team presentation
State rules of competition
Describe your design and its concepts
Include table of class results, sketches, photo/video of boom
How could your current design be improved?

## Slide 30: Closing
Think Safety! Be careful not to poke classmates with the dowels
Have all original data signed by TA
Submit all work electronically
Clean up workstations
Return all unused materials to TA
GOOD LUCK!