## Slide 1
EG1003: Introduction to Engineering and Design
Lemon Car Competition

## Slide 2
Overview
Experimental Objective
Background Information
Materials
Procedure
Assignment
Conclusion

## Slide 3
Experimental Objective
Determine potency of reducing agents
Create chemical cells to generate electricity
Use capacitors to store/release energy
Build car powered by chemical reaction

## Slide 4
Background Information
Fundamental ideas
Redox (reduction/oxidation) reactions
Batteries
Designing citrus cell batteries
Capacitors

## Slide 5
Fundamental Ideas
Electronegativity: measure of element’s attractions of another’s electrons
Ionization energy: energy to remove electron from atom and form a cation
Both properties
Increase:
left to right
bottom to top

## Slide 6
Redox Reactions
When a reaction can be separated into oxidation and reduction:
Oxidation: electron loss
ex: Mg  Mg+2 + 2e-
Reduction: electron gain
ex: O2 + 4e-  2O-2

## Slide 7
Batteries
Battery arrangement
Series circuit increases voltage
Parallel circuit increases current

## Slide 8
Capacitors
Store electrical energy
1F (Farad) Polarized Capacitor
Positive
Negative

## Slide 9
Capacitor Charging
Capacitor charge limit is restricted by charge voltage
Maximizing applied voltage maximizes energy stored
Capacitor is charged in time increments called the time constant (tau):
τ =RC
R=resistance C=capacitance

## Slide 10
Percentage Charged
Charge is logarithmic
It takes approximately 4τ to charge the capacitor
Ex:

## Slide 11
Designing of Citrus Cells
A citrus cell/battery
  Uses two different electrodes
  Citrus acid used as electrolyte

## Slide 12
Electrolytic Solutions
Non-metallic part of circuit
Electrolytes dissociate free ions to create an electrically conductive solution
Lemon Juice used as electrolyte

## Slide 13
Materials
Lemons
Lemon Juice
Magnesium
Copper
Zinc
Nickel
Aluminum
3 Alligator Cable Sets
1 Farad 5.5v Capacitor
Standard Lego Car Chassis
Lego to Alligator Cable Clip Connector
Light Emitting Diode(LED)
Small Cups
Scissors
Tape
DMM (Digital Multi Meter)
Large Plates
Sandpaper

## Slide 14
Procedure
Part 1
    Determine voltage potential of electrodes
    Determine positive and negative poles
Part 2
    Light up LED using two lemon cells with most potent electrode pairs
Part 3
    Decide on the power source
    Chemical cell or capacitor
    Design/Build your car to accept power source

## Slide 15
Procedure
Procedure
Part 1
  Acquire Materials
  Squeeze/roll lemon
  Insert electrodes into lemon ½ cm from each other
  Connect electrodes to DMM
    Record Voltage
    Determine polarity of lemon cell

## Slide 16
Procedure
Part 2
Create second citrus cell
Connect two citrus cells in series
Attach to LED
Is it lit?

## Slide 17
Procedure
Part 3
  Choose your electrodes (remember cost)
  Design your power source
    Chemical or capacitor
  Design car for power source
    Allow 15 min for capacitor to charge
  Create a sketch/pricelist
  TA must sign your work
  Enter competition

## Slide 18
Competition
Factors that will effect the CR (Competition Ratio) are:
  Distance (linear) traveled in a max of 60 seconds
  Cost of components
Item | Cost
Capacitor | $1.00
2oz Lemon Juice (with cup) | $0.25
1.5" Mg Strips | $1.00
Cu Strip | $0.25
Zn Strip | $0.50
Al Strip | $0.25
Ni Strip | $0.25
Lemon Car Components | $0.00
Cost List

## Slide 19
Assignment: Report
Team report
Title page
Discussion topics in the manual
Scan in data and lab notes
  (ask TA for assistance)

## Slide 20
Assignment: Presentation
Team presentation
Include photos of the lemon car
Explain how the battery works

## Slide 21
Conclusion
Return all electrodes to TA
Clean up all materials
TAs will tabulate competition results
Extra credit awarded according to manual