## Slide 1
EG1003: Introduction to Engineering and Design
Product Evaluation & Quality Improvement

## Slide 2: Overview
Objectives
Background
Materials
Procedure
Report
Closing

## Slide 3: Objectives
Build a robot and test it against the EG standards for accuracy and precision
Demonstrate the importance of product evaluation
Disassemble the robot and make quality improvements to the design

## Slide 4: Design Analysis
Engineers perform prototype testing
  Look for improvement suggestions
  Continuously improves product quality
Tests are performed to a company standard
  If the standard is met, the product is acceptable
  If standard not met, product may be redesigned or withdrawn

## Slide 5: Accuracy & Precision
Accuracy:
  Comparison of the average of the results to the standard
Precision:
  Repeatability of the results
  How close are the results to each other?

## Slide 6: Accuracy & Precision
Accurate
Imprecise
Inaccurate
Imprecise
Inaccurate
Precise
Accurate
Precise

## Slide 7: Accuracy & Precision
Distance test B=0.0972
Angle of Deviation test B=0.0323
%Acc = Percent Accuracy Ps = Standard Value Ap = Value Measured
%Prec = Percent Precision B = Exponential Decay Factor P = Actual Precision

## Slide 8: Accuracy & Precision
Distance Test:
    Ps= x 4
Angle of Deviation Test
  Ps= 360°

## Slide 9: Quality Improvement
Analyzing the design
Testing the design
  Through physical or mathematical modeling or computer modeling
Does the robot perform to standard?
  If no, what can be done to improve its functionality?
  If yes, what can be done to improve its performance beyond the standard??

## Slide 10: Reverse Engineering
Understanding how a product functions
  Disassembly of said product
  Noting the key components
Reverse Engineering is carried out in both software and hardware fields

## Slide 11: Gears
Used to manipulate torque and speed
Torque & speed are inversely proportional
Velocity ratio equals inverse of gear ratio
Values for Output and Input are the diameters (or the number of teeth) of the respective gears
Notes: Fix: gear ratio = output/input

## Slide 12: Gears
There are many different types of gears
  Crown, worm, spur, rack, idler gears
Full description of each type of gear can be found on EG Manual
Please take note of gear and velocity ratios since they are extremely useful with SLDP robots

## Slide 13: Materials
Mindstorms Kit
Computer with Mindstorms Software
Protractor and Ruler
Graph Paper

## Slide 14: Procedure
Build a robot according to the robot provided by your TA
Program robot to perform two tests
  Distance
  Angle of Deviation
Determine whether or not robot meets the 80% EG Standard
Reverse engineer the robot and make quality improvements to the design

## Slide 15: Procedure – Distance/Angle Test
Distance & Angle tests are performed at the same time
Create distance/angle test program.
Download distance program to NXT
Run program for 5 seconds on testing paper to determine testing standard
Change program to run for 4 seconds
Record five trials

## Slide 16: Procedure – Distance/Angle Test

## Slide 17: Procedure – Distance/Angle Test
Assess Robot design from data collected and from observations
Make necessary adjustments
Retest robot and collect data
Take pictures of both original design and finalized design

## Slide 18: Procedure – Reverse Engineering
Visually assess the robot's design. Consider how it works
Sketch the front, top, and most detailed side of the robot. Be sure to include dimensions in your sketch. Also sketch the most detailed view of the gear train.
Before disassembling the robot, ask the TA to take a picture of it, or take one yourself

## Slide 19
Disassemble the robot. Analyze its inner workings and sketch the gear train(s)
All sketches in EG1003 must be done in pencil
Have all sketches and original data signed by your TA
Procedure – Reverse Engineering

## Slide 20: Tabulation of Results
Tabulate Results in a chart:
It must pass all the tests at a rate of at least 80%
 | Accuracy | % Acc | Pass/Fail | Precision | % Prec | Pass/Fail
Distance Test |  |  |  |  |  | 
Angle of Deviation Test |  |  |  |  |  | 

## Slide 21: Report
Individual Lab Report
Title page
Discussion topics in the manual
Include original data with TA’s signature
MUST include spreadsheet with test results, standard, average, accuracy, and precision of each test

## Slide 22: Presentation
Team presentation
Follow “Your Assignment” guidelines on EG Manual
Include photos of robot
  TA will assist with digital camera if needed

## Slide 23: Closing
Share tasks – one team member to program; another to build
Have all original data signed by TA
Remember to submit all work electronically
  Submit testing paper to TA at beginning of next lab
Disassemble robot and sort parts into the kits.
Return all unused materials to TAs