## Slide 1: PROTOTYPING WITH MICROCONTROLLERS, SENSORS & MATERIALS
EG1003 | LAB 3

## Slide 2: OVERVIEW
Objective
Background Information
Materials
Procedure
Competition Rules
Assignment
Closing
1
Figure 1: Prototyping with Arduino Board

## Slide 3: OBJECTIVE
To utilize electrical components, an Arduino board, and the Arduino IDE to:
  Control an LED with and without a button
  Test a design prototype
To design a device to slow the rate of heat loss
Enter the device into a competition to obtain the lowest minimal design ratio
2

## Slide 4: BACKGROUND INFORMATION
Prototyping – process of designing and building an early model of a product
Electricity – the movement of electrons
  Current [A] – flow of electrons
  Voltage [V] – difference in charge
  Resistance [Ω] – opposition to current
  Ohm’s Law:
Figure 2: Ohm’s Law Courtesy of Instructables
3

## Slide 5: BACKGROUND INFORMATION
Common electrical components:
  Breadboards
  DC voltage sources
  Resistors
  Push-buttons and switches
  Diodes and transistors
  Light emitting diodes
Figure 3: Electrical Components Courtesy of Wikipedia
4

## Slide 6: BACKGROUND INFORMATION
Breadboards
  Small boards used for circuit prototyping
  Allow temporary connection between circuit components
  Power rails connected vertically (Sections A & D)
  Non-colored rows connected horizontally (Sections B & C)
Figure 4: Breadboard Diagram
5

## Slide 7: BACKGROUND INFORMATION
DC voltage sources – power circuits with voltage difference
Resistors – reduce the current flowing through a circuit
  Color-coded to indicate resistance value
  Thermistor – thermal resistor used to measure temperature
Figure 5: DC Voltage Source (Left), Thermistor (Top Right), and Resistor (Bottom Right)
6

## Slide 8: BACKGROUND INFORMATION
Push-buttons and switches – interrupt or divert current
Diodes and transistors – allow current to pass in only one direction
Light emitting diodes (LEDs) – diodes that use low voltage and current
Figure 6: Push-Button (Top Left), Switch (Top Right), LED (Bottom Left), and Transistor (Bottom Right)
7

## Slide 9: BACKGROUND INFORMATION
Microcontroller – inexpensive, programmable computer
  3.3V – typically used to power low-voltage sensors
  5V – most common power pin used to power circuits
  GND – ground pin (0 V)
  VIN – voltage-in can be used to power the board using a battery
Figure 7: Arduino RedBoard
8

## Slide 10: BACKGROUND INFORMATION
Arduino IDE – program to edit, compile, and upload code to the Arduino board
Code written in the Arduino programming language (based on C/C++)
9
Figure 8: Arduino IDE

## Slide 11: BACKGROUND INFORMATION
Datatypes – different kinds of data values
  e.g. int, double, char
Operators – perform operations on variables and constants
  e.g. +, =, ==, <=
Variables and constants – hold data according to datatype
Figure 9: Examples of Constants and Variables
10

## Slide 12: BACKGROUND INFORMATION
Conditional statements – run code enclosed by curly brackets when condition is met
Figure 10: Conditional Statements
11

## Slide 13: BACKGROUND INFORMATION
Loops – runs section of code repeatedly
  While loops – runs code until the end condition is met
  For loops – runs code for a specific number of times
Figure 11: While and For Loops
12

## Slide 14: BACKGROUND INFORMATION
Tinkercad
  www.tinkercad.com
    Log-in with Autodesk account
  Cloud-based 3D modeling software
  Used to create CAD models, simulate circuitry, and code virtually
Figure 12: Example TinkerCAD Template
13

## Slide 15: BACKGROUND INFORMATION
Heat – form of energy
Heat transfer – process of thermal energy moving from one body to another
  Conduction – through solids
  Convection – within a fluid medium (liquid or gas)
  Radiation – emitted energy in all directions with or without a medium
Figure 13: Modes of Heat Transfer Courtesy of Mr. Oey’s Science Classes
14

## Slide 16: BACKGROUND INFORMATION
Thermodynamic system – defined area in the Universe separated by a boundary
  Open – transfers mass and heat
  Closed – only transfers heat
  Isolated – cannot transfer mass or heat
Figure 14: Open (Left), Closed (Center), and Isolated (Right) Systems Courtesy of x-engineer.org
15

## Slide 17: MATERIALS
Arduino RedBoard and USB cable
Computer with Arduino IDE
Breadboard
Jumper wires
220 Ω resistor
10 kΩ resistor
LED
Push-button
Thermistor
16
Figure 15: Prototyping with Breadboard Courtesy of SparkFun

## Slide 18: PROCEDURE
Remote students will complete Part 1 and 2 on Tinkercad
Part 1: Build an LED and button circuit
Part 2: Thermal insulation device competition
  Goal is to slow heat loss from a heated jar of beeswax
  Add code to the Arduino program for the thermistor
  Build the thermistor circuit using the Arduino board
  Design and build a thermal insulating device
  Test the thermal insulating device and analyze the data
17
Figure 16: Jar of Beeswax with Thermistor

## Slide 19: COMPETITION RULES
Competition will be judged by the lowest minimal design ratio (MDR):
  Insulating capacity (IC) is the change in temperature over time of the beeswax
  Cost is the total cost of the insulating device
  TR is the room temperature (obtain from TA)
  TF is the final temperature of the beeswax (obtain from data)
18

## Slide 20: COMPETITION RULES
Table 1: Material Costs for Thermal Insulation Device Competition
Material | Unit | Cost Per Unit
Large foam cup | 1 | $0.50
Lid | 1 | $0.25
Pack of clay | 1 bag | $0.20
Wool fabric | 2 pieces | $0.10
Cotton balls | 3 balls | $0.05
Popsicle sticks | 1 | $0.01
Paper cup | 1 | $0.40
Styrofoam pieces | 5 | $0.05
Tape | 1 ft | $0.10
Aluminum foil | 1 ft2 | $0.30
Plastic wrap | 1 ft2 | $0.02
19

## Slide 21: COMPETITION RULES
Cannot move thermistor placement with respect to the lid
Insulating device cannot be touched while testing
External heat sources are prohibited
Jar of beeswax must be inside the container within 30 seconds of receiving
Jar of beeswax cannot be returned (no restarts)
At least one material must be used in the design of the insulating device
Try not to touch the hot jar or beeswax
20

## Slide 22: ASSIGNMENT
Individual lab report:
  Answer discussion questions in manual
  Include original graph (temperature vs. time) of insulating device
  Provide minimal design ratio calculation
  Provide price list and design improvements
  Include spreadsheet with competition results
  Due at 11:59 PM the night before Lab 4
Team presentation:
  Address discussion points in manual
  Describe the design of the insulating device
21

## Slide 23: CLOSING
Think safety! Don’t touch hot wax or jar
Submit all work electronically
Take pictures of the insulating device
Clean up workstations
Return all unused materials to the TA
22

## Slide 24: CLOSING
In preparation for the next virtual lab, download this software ahead of time:
  eDrawings Viewer
23

## Slide 25: QUESTIONS?