## Slide 1: Hot Air Balloon Competition
Notes: L.Mexhitaj 2009

## Slide 2: Overview
Objective
Background
Materials
Procedure
Report / Presentation
Closing

## Slide 3: Objectives
Demonstrate basic principles of buoyancy and thermodynamics
Use concept of minimal design

## Slide 4: Hot Air Balloon Principles - Buoyancy
Archimedes’ Principle
  Object immersed in fluid is buoyed up by force equal to weight of fluid displaced by object

## Slide 5: Hot Air Balloon Principles - Thermodynamics
Air pressure, volume, and temperature are related via Ideal Gas Law
Raising air temperature at constant volume (balloon envelope) causes air density within to drop
  Excess air will escape
Balloon weighs less than displaced air
  Buoyant forces cause balloon to rise
V =Volume
P = Pressure
n = # of Moles of Air
T = Absolute Temperature (Kelvin)
R = Gas Constant (0.0821 L atm/mol K)
Ideal Gas Law:

## Slide 6: Components of Hot Air Balloon

## Slide 7: Problem Statement
Design/construct balloon
  Maximize payload (paperclips)
  Maximize flight time
  Minimize cost
Materials must be “purchased”

## Slide 8: Competition Rules
Add paperclip payload to finished design
TA positions balloon above personal heater, releases when balloon temperature stabilizes
Time aloft and # of paperclips recorded by TA
  TA times flight duration with a stopwatch/timer
  Balloon must rise from release point & fly for at least 1 second
Competition ratio used to judge design
  Team with highest ratio wins
  3 trials maximum: design changes permitted (cumulative cost)
Note: Payload is equal to # of paperclips
Balloon Ratio:

## Slide 9: Materials
Tissue paper
8½ " x 11" paper
Drawing paper
Kevlar string
Plastic straws
Plastic tape
Glue stick
Scissors
Paper clips
Personal heater

## Slide 10: Material Price List
Tissue paper………………………..$0.10/sheet
8½" x 11" paper…………..……..$0.05/sheet
Drawing paper……………………..$0.10/sheet
Kevlar string..……………….……..$0.05/ft
Tape……………………………………$0.03/ft
Plastic straws……………………….$0.00

## Slide 11: Procedure
Assess provided materials
Brainstorm possible designs
Sketch design on paper
  Maximum allowable balloon size of 1m3
  Label properly
  TAs must initial sketches
  Major design revisions must also be initialed

## Slide 12: Procedure
Create price list detailing your design
Materials must be “purchased” from TA
  Unused materials will not be refunded
Construct design based on initialed sketch
  Note design changes
Have TA photograph final flight configuration
  Still shot or video

## Slide 13: Assignment: Report
Individual Lab Report
  Bonus for A, B, C, D/H, E, and G Sections
  Required for HS Sections
Title Page
Discussion topics in the manual
Include original data with TA’s signature
Include class results and photo of balloon

## Slide 14: Assignment: Presentation
Team presentation
State rules of competition
Describe your design and its concepts
Include table of class results and photo/video of balloon
How could your current design be improved?
Refer to “Creating PowerPoint Presentations” found on EG website

## Slide 15: Closing
Have all original data signed by TA
Submit all work electronically
Return all unused materials to TA

## Slide 16: GOOD LUCK!