## Slide 1: PROCESSES & WATER FILTERS (VIRTUAL)
EG1003 | LAB 8

## Slide 2: OVERVIEW
Objective
Background Information
Materials
Procedure
Assignment
Closing
1
Figure 1: Hudson River Courtesy of Hudson River Foundations

## Slide 3: OBJECTIVE
To understand the processes behind a water treatment system
To design an efficient water filter
To design a process flow diagram of an industrial-scale water filter
2

## Slide 4: BACKGROUND INFORMATION
3
Figure 2: Water Treatment System Courtesy of the CDC
Water treatment system:
Coagulation & flocculation – addition of chemicals to create flocs
Sedimentation – flocs settle to bottom
Filtration – physical removal of flocs
Disinfection – kills bacteria, viruses, and parasites
Storage – store in water tank

## Slide 5: BACKGROUND INFORMATION
pH – measure of acidity and alkalinity
  Logarithmic scale of concentration of hydrogen ions
  Below 7 is acidic, 7 is neutral, over 7 is basic (alkaline)
  Ideal pH for drinking water is 6.5 – 8.5
Figure 3: Examples of pH Courtesy of Vecteezy
4

## Slide 6: BACKGROUND INFORMATION
Figure 4: pH Scale (Left) and pH Strips (Right) Courtesy of Bradford Derustit
5
pH strip – strip of filter paper that changes color based on pH

## Slide 7: BACKGROUND INFORMATION
Process flow diagram (PFD) – relays information about a process design
  Process vessel & equipment
  Process and utility lines
  Full energy and material balance
  Composition of every stream
  Bypass and recycle streams
Figure 5: Simple PFD Courtesy of InformIT
6

## Slide 8: BACKGROUND INFORMATION
Mass balance – the conservation of mass applied to a process
  Whatever comes in must come out
  Input + Generation = Output + Consumption
Figure 6: Simple Mass Balance Courtesy of NYU
7

## Slide 9: BACKGROUND INFORMATION
Example process:
Three streams enter a mixer:
  500 kg/s pineapple juice
  100 kg/s frozen strawberries
  75 kg/s fresh peaches
Figure 7: First Process Unit Example
8

## Slide 10: BACKGROUND INFORMATION
Next, product stream enters a strainer:
  20% exits as solid and goes into the trash
  80% exits as liquid extract
Figure 8: Second Process Unit Example
9

## Slide 11: BACKGROUND INFORMATION
Figure 9: Third Process Unit Example
10
Lastly, liquid extract enters another mixer with another stream:
  700 kg/s club soda
  Product stream then enters storage unit

## Slide 12: BACKGROUND INFORMATION
Figure 10: Complete Process Flow Diagram Example
11
Combine all the parts to make the complete PFD

## Slide 13: MATERIALS
Computer with internet access
Materials used in the virtual simulation:
  pH strips
  Contaminated water
  Beaker
  Scale
  Alum
  Sodium bicarbonate
  Glass stirring rod
12

## Slide 14: PROCEDURE
13
Part 1: Balance the pH of the contaminated solution
  Access the virtual simulation here
Part 2: Design and test three water filters
  Access the virtual simulation here
  Record data on Excel datasheet
Part 3: Design a process flow diagram based on the best water filter design

## Slide 15: DESIGN CONSIDERATIONS
Water filter design is judged by a competition ratio (CR):
Design must include at least three materials
Design may include at most three of each material
Each design will only be allowed one trial
14

## Slide 16: DESIGN CONSIDERATIONS
15
Material | Unit | Cost Per Unit
Gravel | 1 scoop | $0.25
Sand | 1 scoop | $1.00
Activated Carbon | 1 scoop | $0.50
Table 1: Cost List for Water Filter Design

## Slide 17: ASSIGNMENT
16
Team lab report:
  Answer discussion questions in manual
  Include pictures of water filter designs
  Include Excel datasheet with results
  Include picture of complete process flow diagram
  Due at 11:59 PM the night before Lab 9
Team presentation:
  Address discussion points in manual
  Include cost of water filter designs

## Slide 18: CLOSING
17
Record all data in Excel datasheet
Take pictures/screenshots of the filter designs, contaminated water, filtered water, and process flow diagram
Submit all work electronically

## Slide 19: QUESTIONS?