## Slide 1: Sensors

## Slide 2
Overview
Objective
Concept
Materials
Procedure
Report/Presentation
Closing

## Slide 3
Objective
Design sensor programs
  Mindstorms: Use sensors to stop a motor when a red ball is detected
Apply sensors to Semester-Long Design Project

## Slide 4
Concept: Control Systems
System created to read and analyze data
Use analyzed data for appropriate action
Examples:
  Thermal controls
  Lighting systems
  Alarm systems
  Motion sensors

## Slide 5
Concept: Switches
Switches
  Allow program to perform different actions depending on a certain condition
  If “Condition A” then “Action A” else “Action B”

## Slide 6
Concept: Loops
Loops
  Allow program to run part of a code multiple times as long as a certain condition is met
  While “Condition A” do “Action 1”

## Slide 7
Concept: Sensors
Sensors
  Read data from test environment
  Data converted to digital format for computer
Some sensor types:
  Light
  Temperature
  Ultrasonic
  Touch
Sensors connect to different control devices:
  LEGO -> EV3
  Thermocouple -> DAC -> PC

## Slide 8
Concept: Light Sensor
Measures:
  Color
  Ambient light intensity
  Reflected light intensity
Is used as the condition in the switch for a line follower
  For example: if “reflected light intensity < 5” then “move motor 1” else “move motor 2”

## Slide 9
Concept: Gyro Sensor
Measures:
  Current angle
  Rate at which it is turning
Is used as the loop condition
  While “gyro angle reads < 75 degrees” “move motor”
(not used in this lab)
Needs to be reset before each use

## Slide 10
Concept: Ultrasonic Sensor
Measures:
  Distance to some objects (cm or in)
Is used similarly to the light sensor (switch statement condition)

## Slide 11
Materials
Mindstorms sensor program
  EV3
  Test assembly
  Computer with Mindstorms
LabVIEW sensor programs
  Computer with LabVIEW & DAC
  Thermocouple

## Slide 12
Procedure: Rotation Sensor
Write a program that moves the robot forward for 3 sec
  Add a code that reads the number of rotations during the 3 sec
Write a program that displaying the number of rotations, but the stops robot after 3 rotations

## Slide 13
Procedure: Ultrasonic Sensor
If the sensor detects a distance greater than 40 in, a happy face should appear, for a distance of less than 40 in, a sad face should appear
If the sensors detect a distance less than 40 in but greater than 30 in, a caution sign should appear. But for a distance less than 40 in but greater than 30 in, a sad face should appear

## Slide 14
Procedure: Touch Sensor
Write a program in which your robot would move when the touch sensor is pressed, and would stop when the touch sensor was released

## Slide 15
Procedure: Light Sensor
Write a program for obtaining the light intensity and displaying it on the EV3’s screen

## Slide 16
Report/Presentation
No report for this lab
No presentation for this lab
Milestone due next recitation

## Slide 17
Closing
Have all lab notes signed by TA
Each team member should have a turn using the software
Return all unused materials to TAs

## Slide 18
Sensors
QUESTIONS?