## Slide 1: SUSTAINABLE ENERGY VEHICLE COMPETITION
EG1003 | LAB 10

## Slide 2: OVERVIEW
Objective
Background Information
Materials
Procedure
Assignment
Closing
1
Figure 1: Renewable Energy Sources Courtesy of Physics World

## Slide 3: OBJECTIVE
Evaluate energy storage devices
Analyze different sources of renewable energy
Design a sustainable energy vehicle to enter in a competition
2

## Slide 4: BACKGROUND INFORMATION
Renewable energy – energy harnessed from naturally replenished resources
Figure 2: Renewable vs. Non-Renewable Energy Sources Courtesy of Solar Schools
3

## Slide 5: BACKGROUND INFORMATION
Solar panels – convert sunlight to electrical energy
  Incident sunlight excites electrons to next energy level, emitting energy
  Usually made of silicon
Figure 3: How Solar Panels Work Courtesy of Good Energy
4

## Slide 6: BACKGROUND INFORMATION
Wind turbine – converts wind energy to electrical energy
  Wind causes pressure difference on turbine blades
  Utilizes gear ratios to power generator
Figure 4: How Wind Turbines Work
Courtesy of Tech-Addict
5
Notes: Rotating blades turn a low-speed shaft to a gearbox, which outputs power to an electrical generator through a high-speed shaft.

## Slide 7: BACKGROUND INFORMATION
Capacitor – stores charge temporarily
  Are polarized
  Charged logarithmically (initially charges very fast but rate of charging slows down)
Figure 5: Polarized Leads of 1 Farad Capacitor
6
Positive
Negative

## Slide 8: BACKGROUND INFORMATION
Symbols for common electrical components:
  Battery
  Capacitor
  DC source
7
  Voltmeter
  Ammeter

## Slide 9: BACKGROUND INFORMATION
Series circuit
  Current is equal across components
  Voltage across each component:
8
Parallel circuit
  Current varies across components
  Voltage across each component:
Figure 6: Series Circuit
Figure 7: Parallel Circuit

## Slide 10: BACKGROUND INFORMATION
Digital multimeter – reads current and voltage across circuits
  Measure current in series, called ammeter
  Measure voltage in parallel, called voltmeter
9
Figure 8: Circuits for Using a Multimeter

## Slide 11: MATERIALS
Horizon wind-turbine
Sunforce 50013 1 W solar battery charger
Adjustable table fan
Heat lamp
3V power supply
Digital multimeter
Music voltmeter
9V DC motor
1 F 2.7 V capacitors
3 alligator clip sets
Standard LEGO kit
LEGO to alligator clip connector
Scissors
10
1 Farad 2.7V Capacitor

## Slide 12: PROCEDURE
11
Part 1: Test the power storage device
  Charge a capacitor
  Test capacitors in series and parallel
Part 2: Test the assigned power source using music voltmeter
  Solar panel
  Wind turbine
Part 3: Design a sustainable energy vehicle using the power source of choice and enter in competition

## Slide 13: COMPETITION RULES
Competition is judged by the competition ratio (CR):
The sustainable energy vehicle must carry the power source
Capacitors can only be charged for one minute using the provided power sources
A minimum of 2 capacitors must be used
Each design will only be allowed one trial
Cannot touch vehicle once trial has started
The trial will end after five minutes or when the car stops moving
12

## Slide 14: COMPETITION RULES
13
Material | Unit | Cost Per Unit
Horizon Wind Turbine | 1 | $7.50
Solar Panel | 1 | $10.00
1 F 2.7 V Capacitor | 1 | $3.00
Alligator Clip Set | 1 pair | $0.50
LEGO Kit (Limit One Per Design) | 1 | $0.00
LEGO to Alligator Clip Connector | 1 | $0.10
Tape | 1 foot | $0.10
Table 1: Cost List for Competition

## Slide 15: ASSIGNMENT
14
Team lab report:
  Answer discussion questions in manual
  Include picture and explanation of vehicle design
  Include spreadsheet with power source data and competition results
    Address how measurements from power sources impacted the design
  Due at 11:59 PM the night before Lab 11
Team presentation:
  Address discussion points in manual
  Include cost of vehicle design

## Slide 16: CLOSING
15
Measure current in series and voltage in parallel
Submit all work electronically
Take pictures of the vehicle design
Clean up workstations
Return all unused materials to the TA

## Slide 17: QUESTIONS?