## Slide 1
PROTOYPING A THERMAL INSULATION DEVICE WITH MICROCONTROLLERS AND SENSORS
LAB 3
EG 1004 Introduction to Engineering & Design

## Slide 2
OVERVIEW
Figure 1: Prototyping with Arduino Board
Objective
Background Information
Materials
Procedure
Competition Rules
IDBE Implementation
Assignment
Closing

## Slide 3
OBJECTIVE
Utilize electrical components, an Arduino board, and the Arduino IDE to:
  Control an LED with a button
  Test a design prototype
To design a device to slow the rate of heat loss
Enter the device into a competition to obtain the lowest minimal design equation

## Slide 4
Prototyping – process of designing and building an early model of a product
Electricity – the movement of electrons
Voltage [V]: Difference in charge
Current [A]: Flow of electrons
Resistance []: Opposition to current
Figure 3: Ohm’s Law Courtesy of Instructables
Ohm’s Law: V = IR
BACKGROUND INFORMATION
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 5
Figure 4: Electrical Components courtesy of Wikipedia
Common electrical components:
  Breadboards
  DC voltage sources
  Resistors
  Push-buttons and switches
  Diodes and transistors
  Light emitting diodes
BACKGROUND INFORMATION
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 6
Figure 5: Breadboard Diagram
BACKGROUND INFORMATION
Breadboards
                Small boards used for circuit prototyping
Allow temporary connection between circuit components
Power rails connected vertically (Sections A & D)
Non-colored rows connected horizontally (Sections B & C)
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 7
Reduce the current flowing through a circuit
Color coded to indicate resistance value
Resistors
Power circuits with voltage difference
DC Voltage Sources
Thermal resistor used to measure temperature
Thermistor
Figure 6: DC Voltage Source (Left), Resistor (Middle), Thermistor (Right)
BACKGROUND INFORMATION
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 8
Allow current to pass in only on direction
Diodes & Transistors
Interrupt or divert current
Push Buttons & Switches
Diodes that use low voltage and current
Light Emitting Diodes
(LEDs)
Figure 7: Push Button (Left),
Switch (Right)
Figure 8: Transistor (Left), LED (Right)
BACKGROUND INFORMATION
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 9
Microcontroller – inexpensive, programmable computer
Commonly used to power circuits
5 V
Typically used to power low voltage sensors
3.3 V
Ground pin (0 V)
GND
Can be used to power board with battery
VIN
Figure 9: Arduino Redboard
BACKGROUND INFORMATION
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 10
Arduino IDE – program to edit, compile, and upload code to the Arduino board
Code written in the Arduino programming language (based on C/C++)
Figure 10: Arduino IDE
BACKGROUND INFORMATION
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 11
Perform operations on variables or constants
(eg.+, =, ==, <=)
Operators
Different data values
(eg. Int, double, char)
Datatypes
Hold data according to datatype
Variables and Constants
Figure 11: Examples of Constants and Variables
BACKGROUND INFORMATION
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 12
Figure 12: Conditional Statements
Conditional Statements
Run code enclosed by curly brackets when condition is met
BACKGROUND INFORMATION
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 13
Figure 13: While and For Loops
Loops
Run sections of code repeatedly
While loops
Runs code until end condition is met
For loops
Runs code for a specific number of times
BACKGROUND INFORMATION
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 14
Figure 14: Modes of Heat Transfer Courtesy of Mr. Oey’s Science Classes
Heat – form of energy
Heat transfer – process of thermal energy moving from one body to another
Through solids
Conduction
Within a fluid medium (liquid or gas)
Convection
Emitted energy in all directions with or without a medium
Radiation
BACKGROUND INFORMATION
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 15
Thermodynamic system – defined area in the Universe separated by a boundary
Transfers mass and heat
Open
Only transfers heat
Closed
Cannot transfer mass or heat
Isolated
Figure 15: Open (Left), Closed (Center), and Isolated (Right) Systems Courtesy of x-engineer.org
BACKGROUND INFORMATION
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 16
Arduino RedBoard and USB cable
Computer with Arduino IDE
Breadboard
Jumper wires
220 Ω resistor
10 kΩ resistor
2.2 kΩ resistor
LED
Push-button
Thermistor
MATERIALS
Figure 16: Prototyping with Breadboard Courtesy of SparkFun

## Slide 17
Part 1: Build an LED and Button circuit
Part 2: Thermal insulation device competition
  Goal is to slow heat loss from a heated jar of beeswax
  Add code to the Arduino program for the thermistor
  Build the thermistor circuit using the Arduino board
  Design and build a thermal insulating device
  Test the thermal insulating device and analyze the data
Figure 17: Jar of Beeswax with Thermistor
PROCEDURE

## Slide 18
COMPETITION RULES
Competition will be judged by the lowest minimal design equation (MDE):
  Insulating capacity (IC) is the change in temperature over time of the beeswax
  Cost is the total cost of the insulating device
  TR is the room temperature (obtain from TA)
  TF is the final temperature of the beeswax (obtain from data)
  10 minute run starts from the same temperature (±1°F) for all groups

## Slide 19
COMPETITION RULES
Table 1: Material Costs for Thermal Insulation Device Competition
Material | Unit | Cost Per Unit
Large foam cup | 1 | $0.50
Pack of clay | 1 bag | $0.20
Wool fabric | 2 pieces | $0.10
Cotton balls | 3 balls | $0.05
Popsicle sticks | 1 | $0.01
Paper cup | 1 | $0.40
Styrofoam pieces | 5 | $0.05
Tape | 1 ft | $0.10
Aluminum foil | 1 ft2 | $0.30
Plastic wrap | 1 ft2 | $0.02

## Slide 20
COMPETITION RULES
Cannot move thermistor placement with respect to the lid
Insulating device cannot be touched while testing
External heat sources are prohibited
Jar of beeswax must be inside the container within 30 seconds of receiving
Jar of beeswax cannot be returned (no restarts)
A minimum of $0.40 must be used in the design of the insulating device
Try not to touch the hot jar or beeswax
10 minute run starts from the same temperature (±1°F) for all groups

## Slide 21
IDBE IMPLEMENTATION
Socially-conscious Engineering
  What is the goal of our designs?
Social, Economic, and Environmental Implications
  Who is involved in the design and who are we innovating for?
  Engineering impacts all areas of daily life
  Connect the following inventions to the above implications: cars, antibiotics, the internet
Figure 18: Socially Conscious Engineers
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 22
ASSIGNMENT
Individual lab report:
  Answer discussion questions in manual
  Include original graph (temperature vs. time) of insulating device
  Provide minimal design ratio calculation
  Provide price list and design improvements
  Include spreadsheet with competition results
  Due at 11:59 PM the night before Lab 4
Team presentation:
  Address discussion points in manual
  Describe the design of the insulating device
LED Circuit Diagram does not need to be included in report or presentation
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 23
CLOSING
Think safety! Don’t touch hot wax or jar
Submit all work electronically
Take pictures of the insulating device
Clean up workstations
Return all unused materials to the TA
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 24
QUESTIONS?