## Slide 1
BOOM CONSTRUCTION COMPETITION
LAB 7
EG 1004 Introduction to Engineering & Design

## Slide 2
OVERVIEW
Objective
Background Information
Materials
Procedure
Competition Rules
IDBE Implementation
Assignment
Closing
Figure 1: Cable-Stayed (Cantilever) Bridge

## Slide 3
OBJECTIVE
Design lightweight boom to hold significant load and minimally deflect
Consider material properties when designing a boom
  Stress and strain
Construct and test boom
Enter boom into competition to obtain highest competition ratio

## Slide 4
BACKGROUND INFORMATION
Lifts and moves heavy objects much heavier than the boom
Examples
Construction cranes
Cantilever bridges
Swing bridges
Boom
Figure 2: Tower Crane Courtesy of Philadelphia Magazine
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 5
BACKGROUND INFORMATION
External force acting on an object per unit cross-sectional area
Stress () =
Stress
Measure of deformation resulting from an applied force
Strain () =
Strain
Lo
ΔL
F
Cross-Sectional Area of Bar (A)
Fixed Support
F = applied force A = cross-sectional area ΔL = change in length Lo = original length
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 6
BACKGROUND INFORMATION
Strain (e)
Stress (s)
Fracture Stress
UTS
{P}
{E}
Stress-strain curve
Key points/regions
  Elastic limit
  Ultimate tensile strength (UTS)
  Fracture stress
  Elastic region {E}
  Plastic region {P}
Elastic Limit
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 7
BACKGROUND INFORMATION
Strain (e)
Stress (s)
Fracture Stress
UTS
{P}
{E}
Point where the material becomes permanently deformed
Elastic Limit
Greatest amount of stress a material can withstand
Ultimate Tensile Strength (UTS)
Point where the material fails
Fracture Stress
Elastic Limit
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 8
BACKGROUND INFORMATION
Strain (e)
Stress (s)
Fracture Stress
UTS
{P}
{E}
Elastic Limit
Material will return to its original shape when load is removed
Elastic Region {E}
Material will permanently deform even after load is removed
Plastic Region {P}
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 9
EXAMPLE DEMONSTRATION
Strain (e)
Stress (s)
Fracture Stress
UTS
{P}
{E}
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 10
EXAMPLE DEMONSTRATION
Strain (e)
Stress (s)
Fracture Stress
UTS
{P}
{E}
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 11
EXAMPLE DEMONSTRATION
Strain (e)
Stress (s)
Fracture Stress
UTS
{P}
{E}
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 12
MATERIALS
Thin dowels (0.8 cm diameter)
Thick dowels (1.1 cm diameter)
3D-printed dowels connectors
Cellophane tape
String

## Slide 13
PROCEDURE
Design a boom to obtain the highest competition equation
Consider the basic mass ratio

## Slide 14
PROCEDURE
Assess materials to design the boom
Construct and test the boom

## Slide 15
PROCEDURE
Figure 4: Setup for Competition

## Slide 16
COMPETITION RULES
Boom must be anchored to the white plastic anchorage
Boom must be anchored in less than two minutes
Boom may not be fixed to anything besides the anchorage
Boom must extend at least 1.5 meters horizontally from the edge of the anchorage
Boom basic weight ratio must be greater than 1
A team can use any number of dowels, as long as their total length is less than or equal to the length of 4 uncut dowels (4 x 122 cm, or 488cm)

## Slide 17
COMPETITION RULES
Make a sketch of your design and get a TA to sign off on it
Anchor time will be timed from when the TA says “go” to when all hands are off the boom
TA will place a holder for the weights at the end of the boom
The boom must start at least 0.30 m from the ground after adding 15 grams of preload
TA will place weights in the holder until the boom deflects 20 cm or fails
Values will be entered into a competition scoresheet which will be available on the EG1004 Website

## Slide 18
IDBE IMPLEMENTATION
Figure 5: Tacoma Narrows Bridge
Engineering Responsibility
  Must uphold industrial and ethical standards
  Risks are large and impact is widespread
  Cost of failure is catastrophic: human life
Case Study: Tacoma Narrows Bridge
  Windy conditions led to bridge oscillations
  Design could not support the elasticity of the vibrations
  Catastrophic failure of the bridge
  No deaths
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 19
ASSIGNMENT
Individual lab report:
  Answer discussion questions in manual
  Include competition scoresheet results
  Include pictures of the boom
  Due at 11:59 PM the night before Lab 8
Extra credit opportunity:
  Can replace a lower grade on Lab 3 report
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 20
ASSIGNMENT
Team presentation:
  Address discussion points in manual
  State rules of the competition
  Include pictures, competition scoresheet, digital sketches
  Due at 11:59 PM the night before the next Recitation
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 21
CLOSING
Think safety! Be careful not to poke classmates with the dowels
Have all original data signed by a TA
Submit all work electronically
Take pictures
Clean up workstations
Return the dowel connectors – do not throw them away
Return all unused materials to the TA
Notes: Tandon Areas of Excellence
Sustainability
Urban
Telecommunications & IT
Health
Artificial Intelligence
Professional Skills & Tandon Resources
MakerSpace & RAD
Teamwork & Vertically Integrated Projects
Career Services
Project Management & Technical Writing
World Trade Center Construction

## Slide 22
QUESTIONS?